## Slide 1: ABS Brakes (Anti-Lock)
History
  Anti-Lock brakes were introduced in the 1970’s as a safety feature on luxury cars.
  They are now required standard safety equipment on all cars.
  They greatly reduce the stopping distance of a car in emergency situations
  They allow the car to be steered even with the brake pedal fully applied
Function
  ABS prevents the tires from locking up and entering a skid.
  Wheel sensors and an on-board computer pulses the brakes to keep the tires rotating whenever a skid is detected.
  Preventing tire skid both maximizes stopping force and maintains steering.

## Slide 2: Dry Asphalt
An old car without ABS is travelling at a speed of 60 km/h on dry asphalt. The car has a mass of 1000kg
  What is the coefficient of friction?
  What is the friction force stopping the car?
  What distance does it take for the car to stop?
Repeat this calculation for a new car with ABS travelling on dry asphalt.

## Slide 3: ABS Brakes (Anti-Lock)
History
  Anti-Lock brakes were introduced in the 1970’s as a safety feature on luxury cars.
  They are now required standard safety equipment on all cars.
  They greatly reduce the stopping distance of a car in emergency situations
  They allow the car to be steered even with the brake pedal fully applied
Function
  ABS prevents the tires from locking up and entering a skid.
  Wheel sensors and an on-board computer pulses the brakes to keep the tires rotating whenever a skid is detected.
  Preventing tire skid both maximizes stopping force and maintains steering.

## Slide 4: Wet Asphalt
An old car without ABS is travelling at a speed of 60 km/h on wet asphalt. The car has a mass of 1000kg
  What is the coefficient of friction?
  What is the friction force stopping the car?
  What distance does it take for the car to stop?
Repeat this calculation for a new car with ABS travelling on wet asphalt.

## Slide 5: Consolidation Questions
How does ABS affect the stopping distance of a car?
How do changing road conditions affect the stopping distance of a car?
How would increasing the number of tires affect the stopping distance?
How would increasing the size of tires affect the stopping distance?
How would changing the tire compound affect the stopping distance?