## Slide 1: Electrical Charge Equations

## Slide 2: Electrons (Smallest Charge)
Electrons e- are:
  The smallest unit of charge
  Moving electrons produce
    Electricity
    Light & Radio Waves
  One electron is extremely weak
  You need a huge amount to do anything!
Protons p+ are:
  The opposite of electron charge
  Don’t usually move much

## Slide 3: Coulomb (Units of Charge)
The Coulomb is
  The Metric Unit for Electric Charge
  Its equation symbol is: "q"
  Its unit symbol is: "C"
  1 C = 6.24x1018 electrons (or protons)
  or 1 electron = 1.60x10-19 C
It is named after:
  Charles Augustin de Coulomb
  A French Physist
  Studied electricity in the 1770's

## Slide 4: Electric Current (I)
Electric Current is:
  The rate of flow of electrons
I = q / Δt
Therefore, Amperes (A) are:
  Coulombs per second
1 A = 1 C/s

## Slide 5: Electric Current (I)
In a 10 A circuit, how many coulombs of charge flow through a light bulb in 1 minute?
I = q / Δt or q = I x Δt
q = 10 A x 60 s
q = 10 C/s x 60 s
q = 600 C

## Slide 6: Electric Potential Difference (V)
Electric potential is a measurement of:
  the electric potential energy of the electrons.
V = ΔE / q
It measures both:
    ΔE – The energy of electrons (where ΔE is measured in Joules "J")
    q – The number of electrons
Electric potential is measured in Volts (V)
1 V = 1 J/C

## Slide 7: Electric Potential Difference (V)
10 C of electrons has 1200 J of energy. What is their electric potential?
V = ΔE / q
V = 1200 J / 10 C
V = 120 J/C
V = 120 Volts

## Slide 8: Electric Energy (ΔE)
Electrical appliances use energy
  ΔE is the energy used (measured in Joules "J")
  ΔE = VIΔt

## Slide 9: Practice Questions

## Slide 10: Electrical Charge Equation Notes:
In physics, q is measured in ___________
1C = ___________ electrons
1 electron = ____________ Coulombs
Electric Current Equation: I = ________
Amperes: 1A = __________
Potential Difference Equation: V = _________
Volts: 1V = ____________
In physics, ΔE is measured in ___________
Electrical Energy Equation: ΔE = _________

## Slide 13
Electric Potential Difference

## Slide 14
Electric Potential Difference