## Slide 1: Electricity Basics – Dec 7
Agenda (60 min):
Presentation: Basic Electrical Units
Energy Unit: Q&A
Upcoming
Energy Unit Test – TOMORROW

## Slide 2: Electric Charge (Q)
The charge of electrons (-ve) and protons (+ve) is the basis of electricity and the electromagnetic force.
We measure charge in Coulombs (C)
  Single electrons are too tiny to matter in circuits
  1 C = 6.2x1018 electrons
The symbol for charge is Q
  Q is measured in Coulombs (C)

## Slide 3: Electric Current (I)
Current is a measure of the flow of electrons
I = Q / Δt
Current is measured in Amperes (A)
1 A = 1 C/s

## Slide 4: Electric Current (I)
In a 10 A circuit, how many coulombs of charge flow through a light bulb in 1 minute?
I = Q / Δt or Q = I x Δt
Q = 10 A x 60 s
Q = 10 C/s x 60 s
Q = 600 C

## Slide 5: Measuring Current
Series Circuit
  The flow of electrons follow only one path
  Itotal = I1 = I 2
Parallel Circuit
  The flow of electrons is divided
  Itotal = I1 + I 2
I total
I total
I 1
I 1
I 2
I 2

## Slide 6: Measuring Current
I total
2A
2A
I total
2A
2A
Itotal = ?
Itotal = ?

## Slide 7: Electric Potential Difference (V)
Electric potential is a measurement of the electric potential energy associated with electrons.
V = ΔE / Q
It measures both:
    ΔE – The energy of electrons
    Q – The number of electrons
Electric potential is measured in Volts (V)
1 V = 1 J/C

## Slide 8: Electric Potential Difference (V)
10 C of electrons has 1200 J of energy. What is their electric potential?
V = ΔE / Q
V = 1200 J / 10 C
V = 120 J/C
V = 120 Volts

## Slide 9: Measuring Potential Difference
Series Circuit
  The energy of the electrons is shared between the loads
  Vtotal = V1 + V 2
Parallel Circuit
  The energy of the electrons is the same for each load
  Vtotal = V1 = V 2
V total
V total
V 1
V 1
V 2
V2

## Slide 10: Measuring Potential Difference
V total
2V
2V
V total
2V
2V
Vtotal = ?
Vtotal = ?

## Slide 11: Electrical Resistance (R)
Electrical resistance is a measure of how difficult it is for electric current to flow through a material.
Ohm’s Law is a useful way to define resistance
R = V / I
Resistance is measured in Ohms (Ω)
1 Ω = 1 V/A

## Slide 12: Electrical Resistance (R)
What is the resistance of a circuit that has a current of 5 A and an electric potential of 120 V?
R = V / I
R = 120 V / 5 A
R = 60 V/A
R = 60 Ω

## Slide 13: Measuring Resistance
Series Circuit
  The resistors add together
  Rtotal = R1 + R 2
Parallel Circuit
  The resistors affect the voltage and current in a more complicated way
  1/Rtotal = 1/R1 + 1/R 2
R 1
R 1
R 2
R2

## Slide 14: Measuring Resistance
2 Ω
2Ω
2 Ω
2 Ω
Rtotal = ?
Rtotal = ?

## Slide 15: Past Due
Samah (p)
Anisha (p) – email t.b.d.
Umesh (p)
Karamjeet (n) - lunch
Katyayani (p,s)
Abdullahi (p)
Anshi (p, s) – email t.b.d.
Ashonjit (p)
Lajanthan (p) - absent
Amandeep (p)
Harjinder (n,s)
Vish (p,n,s)

## Slide 16: Equations
W = FΔd W = ΔE
Ek = ½ mv2 Eg = mgh
Em = Ek + Eg + Ee
P = ΔE/ Δt
Efficiency = (Eout / Ein) x 100%