## Slide 1: Magnetic Force & The Motor Principle
Magnetic Fields & Forces

## Slide 2: Recall – Force Between Two Parallel Wires
Wires Attract When:
  Current is in the same direction
Wires Repel When:
  Current is in opposite directions

## Slide 3: Motor Principle (Fig A & B)
English physicist Michael Faraday (1791–1867) determined that the magnetic field of a permanent magnet can exert a force on the charges in a current-carrying conductor.

## Slide 4: Motor Principle (Fig C)
To the left of the conductor, the field lines point in the same direction and tend to reinforce one another (add), producing a strong magnetic field.
To the right, the fields are opposed and, as a result, tend to cancel one another, producing a weaker field.
Add
Cancel

## Slide 5: Motor Principle (Fig D)
This difference in field strength results in a force to the right on the conductor.
If either the external field or the direction of the electric current were reversed, the force would act in the opposite direction.

## Slide 6: Motor Principle - Definition
A current-carrying conductor that cuts across external magnetic field lines experiences a force perpendicular to both the magnetic field and the direction of electric current.
The magnitude of this force depends on:
  the magnitude of the external magnetic field
  the magnitude of the current,
  the angle between the conductor and the magnetic field it cuts across.

## Slide 7: Right Hand for Magnetic Force
Direction of magnetic force can be determined as follows:
  Thumb points in direction of current
  Fingers point in direction of magnetic field
  Palm of hand points in direction of force
F

## Slide 8: Force on a Wire
When a current-carrying conductor is in an external magnetic field, but is not parallel to the field, it experiences a magnetic force.
Note: When the conductor is parallel to the field there is no force.
N
S
I
N
S
x
Current into Page
I
N
S
B

## Slide 9: Force on a Wire
When a current-carrying conductor is in an external magnetic field, but is not parallel to the field, it experiences a magnetic force.
Note: When the conductor is parallel to the field there is no force.
N
S
I
Force out of Page
F
N
S
x
Current into Page
F
I
N
S
B
No Force I and B
Parallel

## Slide 10: Predict the Force
X X X X X X
X X X X X X
X X X X X X
X X X X X X
I
B into page
A.
• • • • • •
• • • • • •
• • • • • •
• • • • • •
I
B out of page
B.
I
B to the left
C.
• • • • • •
• • • • • •
• • • • • •
• • • • • •
I
B out of page
D.

## Slide 11: Predict the Force
I
E.
B to the left
F.
B to the left
X
•
Current in and out

## Slide 12: Motors & Generators

## Slide 13
Electric motors are used in cooling fans for computers, in refrigerators, in electric cars, in power tools such as electric drills, and even in many remote-controlled toys.
Many subway systems use electric motors as a clean and silent way to power their trains.
Electric Motors

## Slide 14: Simple DC Motor

## Slide 15: Two Pole Motor
Solenoid replaces loop of wire.
Current in solenoid creates North and South pole.
Magnetic attraction and repulsion causes armature to spin.
Commutator reverses current each ½ spin

## Slide 16
Generators operate like motors in reverse.
Mechanical energy from renewable & non renewable sources are used to spin magnets and coils of wire.
Electric current is produced by the spinning magnets and coils.
Electric Generators & Turbines

## Slide 17
Michael Faraday- 1831
Faraday’s Law of Electromagnetic Induction
A changing magnetic field in the presence of a conductor will induce charge to flow in a conductor.
● basis of electric generating turbines
wind
water
steam
Rotates
magnets
Generates
current in conducting coils
● Complement to Oersted’s Law of Electromagnetism
Current
(moving charge)
Magnetic
Field
Oersted
Faraday

## Slide 19
Section 13.5 Questions:
Page 489 #’s 1-8
Read pages 496-498
Practice Questions
Page 498 #’s 1-4

## Slide 20
Motor Principle

## Slide 21
English physicist Michael Faraday (1791–1867) set out to prove that, as a wire carrying electric current could cause a magnetized compass needle to move, so in reverse a magnet could cause a current-carrying wire to move. Suspending a piece of wire above a bowl of mercury in which he had fixed a magnet upright, Faraday connected the wire to a battery, and the wire began to rotate.
Motor Principle

## Slide 22
The motor principle is also used in the definition of the ampere. If two long wires are parallel to each other as in the figure, and electric current is in each, the wires will experience a force, as shown in the figure. One ampere is the current that, when flowing through each of two straight parallel wires placed 1 m apart in a vacuum, produces a force of 2.0 x 10–7 N between the wires for each 1 m of their length.
Motor Principle