## Slide 1: Electric Circuits

## Slide 2: What do you remember?
Term | Definition
____current | Circuit in which elements are connected in line so there is only one path for charges to follow.
____voltage | B. Opposition to the flow of charge.
____load | C. Device which measures electric potential difference.
____switch | The work per unit charge required to move a positive charge between two points in an electric circuit.
____voltmeter | E. Control device in an electric circuit.
____ammeter | F. The rate at which electrical charges flow in a circuit.
____series circuit | G. Circuit in there is more than one path for charges to follow.
____parallel circuit | H. A direct pathway with low resistance connecting two sides of a battery or other electrical source.
____resistance | Device which converts electrical energy into other forms of energy.
____short circuit | J. Device which measures electric current.
____source | K. Device which supplies energy to charges in a circuit.
A
B
C
D
E
F
G
H
I
J
K

## Slide 3: Three key components of an electric circuit:
Source: device which provides electrical
energy to the charges in a circuit
e.g battery , power supply
Load : device which converts electrical
energy to another form
e.g. light bulb, motor
Conductor: provides a pathway for current flow
e.g. wire

## Slide 4: Circuit Symbols and Diagrams
Symbol | Device | Symbol | Device
 | Cell |  | Resistor
 | Battery |  | Variable Resistor
 | AC Voltage Source |  | Light Bulb
 | DC Voltage Source |  | Motor
 | Switch |  | Ammeter
 | Generator |  | Voltmeter

## Slide 5: Draw the circuit below and indicate the direction that positive charge (conventional current) would flow:
Conventional Current Flow: -the direction POSITIVE charges flow in a circuit
+
-
*Electron Flow: in reality, electrons flow in the opposite direction from the negative terminal
Direction of Current Flow:

## Slide 6: Circuit Measurements
Current:
Voltage:
Measured with an __________
connected in line ( in _______) so that current passes directly through the meter.
Measured with a __________
connected across the device ( in _________)
ammeter
series
voltmeter
parallel

## Slide 7: Types of Current
Direct Current (DC): current in which charges flow in one direction
 produced by a battery or DC transformer
Alternating Current (AC): current in which charges change direction periodically
 produced by a wall socket

## Slide 8: Circuit Parameters
Current: Symbol: I Units: Ampere (A)
The total charge that passes a point in the circuit in
given time.
A:
B:
Greater current
Less current

## Slide 9
Analogy: Battery  Pump
Potential Difference or Voltage (V)
We can compare an electric circuit to a water circuit to understand the concept of potential difference and how a battery works:
The pump does work on the water to raising it up by h and increasing its gravitational potential energy.
Similarly, a battery does work on charges to transfer electrical potential energy to the charges.

## Slide 10: Potential Difference, V
Definition: the potential difference between two points in an electric circuit is the work done per unit charge as the charge moves between the two points

## Slide 11: Potential Gain vs. Potential Drop
Battery: Potential _____
Bulb: Potential ______
Vfinal > Vinitial
Vfinal < Vinitial
Gain
Drop