## Slide 1: Friction
Friction: A force that resists the motion of an object across a surface.
Factors That Affect Friction:
  The Normal Force applied by the surface on the object.
  The types of materials in contact.
Note: Factors such as surface area and shape do not affect the force of friction.
FN
Fa
Fg
Ff

## Slide 2: Friction
Friction: A force that resists the motion of an object across a surface.
Factors That Affect Friction:
  The Normal Force applied by the surface on the object.
  The types of materials in contact.
Note: Factors such as surface area and shape do not affect the force of friction.
FN
Fa
Fg
Ff

## Slide 3: Coefficient of Friction
μ is the Coefficient of Friction
Ff = μFN
The Coefficient of Friction is a physical property of the two materials in contact
  Each combination of materials has a different value of μ
  The value of μ is determined by experiment
FN
Fa
Fg
Ff

## Slide 4: Coefficient of Friction

## Slide 5: Kinetic Friction
Kinetic Friction: A force of friction that resists the motion of an object while the object is moving.
μk is the Coefficient of Kinetic Friction
FK = μKFN
If force of friction (Ff) equals FK as long as the object is moving.
FK does not depend on the applied force (Fa)
FK and FS cannot be acting at the same time
μk and μs are usually different for the same combination of materials
FN
Fa
Fg
Ff

## Slide 6: Kinetic Friction – Sample Problem
Find the normal force (FN)
Determine if it is static or kinetic fiction
Look up the coefficient of friction (μ)
Use: Ff = μFN

## Slide 7: Kinetic Friction – Sample Problem
Find the normal force (FN)
    FN = mg FN = (230)(9.81) = 2260 N
Determine if it is static or kinetic fiction
    Kinetic (*** Note: Skidding tires are kinetic)
Look up the coefficient of friction (μ)
    μ = 0.70 (Rubber on Dry Concrete)
Use: Ff = μFN
    Ff = (0.70)(2260) = 1580 N

## Slide 8: Static Friction
Static Friction: A force of friction that prevents an object at rest from starting to move.
μs is the Coefficient of Static Friction
FS(max) = μsFN
If the applied force (Fa) is equal or less than Fs
  Then Ff is equal but opposite to Fa
  And the object does not move.
If the applied force (Fa) is greater than Fs
  Then the object begins to move
  Static Friction no longer applies
FN
Fa
Fg
Ff

## Slide 9: Static Friction – Sample Problem
Find the normal force (FN)
Determine if it is static or kinetic fiction
Calculate the coefficient of friction (μ)
    μ = ? (Asked to calculate Wood on Dry snow)
Use: Ff = μFN

## Slide 10: Static Friction – Sample Problem
Find the normal force (FN)
    FN = mg FN = 5450 N
Determine if it is static or kinetic fiction
    Static (**** Note: “just starting to move”)
Calculate the coefficient of friction (μ)
    μ = ? (Asked to calculate Wood on Dry snow)
Use: Ff = μFN
    μ = Ff / FN μ = 88 / 5450 = 0.016

## Slide 11: Some Final Thoughts
Note that μk is usually less than μs
Can μk be exactly equal to μs?
  Describe the motion as you start pulling on an object initially at rest.
Can μk be greater than μs?
  Describe the motion as you start pulling on an object initially at rest.